## Slide 1: A Programming Model for Efficient Inter-Kernel Control-Flow on Memory-Mapped Near-Data Processing Architecture (WIP)
Seungheon Lee, Wonhyuk Yang, Seonyeong Heo†, Gwangsun Kim
POSTECH | †Kyung Hee University
Notes: Hello, I'm Seungheon Lee from POSTECH, and I'll present our paper "A Programming Model for Efficient Inter-Kernel Control-Flow on Memory-Mapped Near-Data Processing Architecture."

## Slide 2: Overcoming Memory Wall with Near-Data Processing
CXL memory addresses the memory bandwidth & capacity walls
Near-Data Processing (NDP) can overcome the data movement bottleneck
Compute Express Link (CXL)
Memory
Long latency & low bandwidth
 Data movement bottleneck!
NDP
unit
CXL Memory
Memory
Memory
Memory
Host
Memory
Memory
Memory
…
CXL Controller
High BW
Notes: To address the memory bandwidth and capacity walls, CXL memory has been recently proposed. However, accessing CXL memory can incur (Click) long latency and low bandwidth, causing data movement bottleneck. To address this, (Click) near-data processing in CXL memory has been proposed to (Click) utilize higher internal bandwidth.

## Slide 3: Memory-Mapped Near-Data Processing (M2NDP)[1] Architecture
Vectorized NDP kernels are launched from the host
μthreads are mapped to addresses in a μthread pool region
[1]H. Ham, J. Hong et al., Low-overhead General-Purpose Near-Data Processing in CXL Memory Expanders, MICRO’24
μthread
pool region
Vector C
Vector A
Vector B
…
…
…
μthread 0
+
=
μthread 1
+
=
+
=
…
μthread 1024
32 B
32 B
32 B
0xC0020
0xC0000
0xC8000
…
VectorAdd kernel example
M2NDP unit
…
NDP
core
NDP controller
NDP
core
Host
CXL
VectorAdd kernel
Sub-cores
Scratchpad memory
Scalar ALUs
Vector ALUs
Register file
µthread slot
…
µthread slot
NDP core
…
…
Core
M2NDP architecture lacks a high-level programming model!
Notes: In particular, Memory-Mapped Near-Data Processing architecture enables general-purpose NDP in CXL memory by extending the RISC-V architecture. In the NDP kernel, for instance VectorAdd, many μthreads are created and mapped to data chunks in a given memory region called μthread pool region. They execute vectorized kernels with fine-grained multithreading for high parallelism.
(Click) However, the M2NDP architecture lacks a high-level programming model.

## Slide 4: Communication Overhead from Inter-Kernel Control Flow
Host-side iterative, conditional kernel launches in complex workloads
 Significant performance overhead
bool cond;
do {
cond = false;
cudaMemcpy(d_cond, &cond, 1, HostToDevice);
kernel<<<grid, threads>>>(..., d_cond);
cudaMemcpy(&cond, d_cond, 1, DeviceToHost);
} while (cond);
Host code in CUDA
µs-scale latency
(including SW overhead)
launch
Device
Host
while(cond)
kernel
kernel
launch
Time
while(cond)
Host-driven control flow is intuitive but degrades performance!
Notes: Furthermore, complex workloads with iterative and conditional kernel launches can still suffer from the long host-device communication latency (Click) For instance, in CUDA, kernel launch decisions are made by the host, causing (Click) frequent host-device round trips with (Click) microsecond-scale latency including software overheads. Therefore, (Click) such host-driven control flow degrades performance for dynamic workloads.

## Slide 5: Existing Solution: CUDA Graph Approach
CUDA Graph
launch
Device
Host
while(cond)
kernel
kernel
launch
Time
while(cond)
Reduced runtime
cudaGraph_t rootGraph;
cudaGraphCreate(&rootGraph, 0);
cudaGraphConditionalHandle handle;
cudaGraphConditionalHandleCreate(
&handle, rootGraph, 1,
cudaGraphCondAssignDefault);
cudaGraph_t bodyGraph;
cudaGraphNodeParams condParams = {
.type = cudaGraphNodeTypeConditional,
.conditional = {
.handle = handle,
.type = cudaGraphCondTypeWhile,
.phGraph_out = &bodyGraph}};
cudaGraphNode_t whileNode;
cudaGraphAddNode(&whileNode, rootGraph,
NULL, 0, &condParams; void *kernelArgs[] = { ... };
cudaKernelNodeParams kernelParams = {
.func = (void*) kernel,
.gridDim = dim3(...),
.blockDim = dim3(...),
.kernelParams = kernelArgs, ...
};
cudaGraphNode_t kernelNode;
cudaGraphAddKernelNode(&kernelNode,
bodyGraph, NULL, 0, &kernelParams);
void *checkArgs[] = { &handle, ... };
cudaKernelNodeParams checkParams = {
.func = (void*) check,
.gridDim = dim3(...),
.blockDim = dim3(...),
.kernelParams = checkArgs, ...
};
cudaGraphNode_t checkNode;
cudaGraphAddKernelNode(&checkNode,
bodyGraph, &kernelNode, 1, & checkParams);
End
Start
kernel
while
Better performance but with degraded programmability!
Notes: To address this, graph-based approaches like CUDA graph launch multiple kernels (Click) as a task graph. By making kernel launch decisions on the device, (Click) it effectively reduces host-device communication. However, (Click) it requires manual graph constructions as in this example, (Click) substantially degrading programmability.

## Slide 6: Programming Model Requirements for M2NDP
Performant inter-kernel control flow support with good programmability
Unified abstraction for M2NDP-specific architectural features
  E.g., μthread pool region, scratchpad memory
Effective support for writing vectorized NDP kernels
  E.g., built-in methods for accessing mapped data from a μthread
 device_main() for intuitive, device-driven inter-kernel control flow
 Task abstraction with C++ class
 Extended Google’s Highway SIMD library
Arachne: proposed programming model for M2NDP
Notes: For effective NDP programming, we require (Click) a performant and easily programmable inter-kernel control flow support. (Click) In addition, we need a unified abstraction for architectural features like scratchpad memory and uthread pool region (Click) as well as an effective way to write vectorized kernel code. (Click) To this end, we propose device_main() for intuitive, device-driven inter-kernel control flow. (Click) Also, we provide a unified task abstraction based on C++ class. (Click) Moreover, we extend Google's Highway SIMD library for writing vectorized NDP kernels. (Click) The resulting programming model is called Arachne. In the following slides, we will discuss each of these in detail.

## Slide 7: Device-Driven Inter-Kernel Control Flow in Arachne
device_main() intuitively expresses inter-kernel control flow
  Analogous to C/C++ main() except that it runs entirely on the device
  Executed on a lightweight core in the NDP controller
device_main(...) {
...
do {
cond = false;
kernel(cond, ...);
} while (cond);
...
}
…
NDP
core
Memory
Memory
…
NDP controller
NDP
core
Core
Host
CXL
Notes: The “device-main" function enables intuitive and efficient inter-kernel control flow. (Click) It is analogous to the main() function of C++ but is entirely executed on (Click) a lightweight core in the NDP controller.

## Slide 8: Comparison with Existing Programming Models
Programmability
Performance
Host-driven
control flow
Graph-based
control flow
Proposed
device-driven
control flow
Intuitive inter-kernel control-flow expression
Reduced
host-device
communication
Notes: This plot compares the performance and programmability of different approaches. (Click) Compared with the host-driven control flow, we reduce host–device communication for better performance. (Click) Also, compared with the graph-based control flow like CUDA graph, we improve programmability.

## Slide 9: Task Abstraction with C++ Class
Base class NDPTask for common methods and variables
#pragma m2ndp NDPTask Base
template <typename T>
class NDPTask {
public:
virtual void launch(T *base, size_t bound,
bool sync, void *args) final;
virtual void synchronize() final;
...
protected:
virtual void device_main(void *args) = 0;
T* uthr_pool_base;
size_t uthr_pool_size;
...
};
Host-callable
built-in runtime APIs
Common task components
e.g., device_main(),
μthread pool region
Notes: Furthermore, we provide a unified abstraction of NDP tasks or programs based on C++ class. The base NDPTask class bundles elements that are shared across all tasks — (Click) it exposes host-callable runtime APIs, (Click) and holds common components like device_main() and the μthread pool region.

## Slide 10: Declaring a Specific NDP Task
#pragma m2ndp NDPTask
class MyTask : NDPTask<float> {
private:
void device_main(void *args) override;
parallel void kernel(...);
serial void kernel2(...);
scratchpad float mydata[8];
};
Task-specific components
- NDP kernels
- Scratchpad memory
- Definition of device_main()
Inherit from base class
void MyTask::device_main(void *args) {
bool cond;
kernel(cond, ...);
if (cond)
kernel2(...);
}
Notes: To declare a specific NDP task, users simply inherit from this base class and define the task-specific components — NDP kernels, scratchpad memory, and the definition of device_main(). This provides a unified abstraction for the features of the M2NDP architecture.

## Slide 11: Extending Google Highway[2] for Kernel Programming
Added support for M2NDP-specific features
  Identifying μthread and accessing mapped data chunk
  Vector atomic memory operations
SPMD approach: single code for all μthreads of a kernel
[2]Highway, a C++ library that provides portable SIMD/vector intrinsics, Google. https://github.com/google/highway
void VectorAdd::kernel(int *a, int *b) {
HWY::Simd<int, 8> D;
auto va = HWY::Load(D, NDP::AddOffset(a));
auto vb = HWY::Load(D, NDP::AddOffset(b));
auto vc = HWY::Add(va, vb);
NDP::StoreToChunk(D);
}
μthread
=
+
32 B
b
c
a
Example NDP kernel
…
…
…
…
…
…
μthread pool
Notes: Finally, we extend Google’s Highway SIMD library for expressive vector kernel programming in M2NDP. We added methods for identifying μthread, accessing mapped data chunk, and vector atomic memory operations. (Click) An NDP kernel is written in an SPMD manner — single code for all μthreads of a kernel. (Click) As an example, this vector-add kernel loads two vectors, adds them, and stores the result to the mapped chunk.

## Slide 12: Evaluation Methodology
Evaluation on M2NDP simulator
  Baseline (host-driven control flow) vs. preliminary Arachne implementation
Workload: Single-Source Shortest Path (SSSP)
  Representative for iterative, data-dependent kernel launches
Notes: We evaluated an early implementation of Arachne on the M2NDP simulator, comparing it against a host-driven baseline. For this, we chose single-source shortest path, since it has frequent inter-kernel control flow.

## Slide 13: Effect of Device-Driven Control Flow
Arachne achieved up to 8.3× speedup compared with baseline.
Chart: Speedup
| 0.5 | 2 | 8 | 0.5 | 2 | 8 | 0.5 | 2 | 8 | 25K | 50K | 100K
Baseline | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Arachne | 1.4947 | 2.945 | 8.267 | 1.2325 | 1.9901 | 4.8998 | 1.1043 | 1.4611 | 2.9125
Communication latency
Graph size
25K nodes
0.5 μs 2 μs 8 μs
50K nodes
0.5 μs 2 μs 8 μs
100K nodes
0.5 μs 2 μs 8 μs
Notes: Arachne achieved up to 8.3 times speedup over the baseline host-driven control flow model.
(Click) The performance gain increases as the host-device communication latency increases, since Arachne reduces such communication.
(Click) On the other hand, the performance gain decreases as the graph size increases, since the kernel runtime becomes more dominant.

## Slide 14: Summary
Existing programming models trade off programmability and performance in inter-kernel control flow
Arachne enables effective NDP offloading through:
  Device-driven control flow via device_main()
  Class abstraction of NDP tasks
  Highway extended for M2NDP
Arachne achieved up to 8.3× speedup for SSSP over host-driven inter-kernel control flow while enabling intuitive kernel programming for M2NDP
Ongoing work:
  Evaluate Arachne with additional diverse workloads
  Support asynchronous kernel launches in device_main()
Notes: (Summary.) In summary,
Existing programming models trade off programmability and performance in inter-kernel control flow. Arachne enables effective NDP offloading through Device-driven control flow via device_main(), Class abstraction of NDP tasks, and Highway extended for M2NDP. As a result, Arachne achieves up to 8.3× speedup for SSSP over host-driven control flow, while enabling intuitive kernel programming for M2NDP.
As ongoing work, we plan to evaluate Arachne with additional diverse workloads, and support asynchronous kernel launches in device_main().

## Slide 15: Q&A
Notes: Thank you for listening. I'd be glad to take any questions.

## Slide 16: Backup Slides

## Slide 17: Highway SIMD Library
Google’s Highway SIMD Library enables portable SIMD programming in C++ by providing target-agnostic SIMD operations wrapping with target-specific SIMD intrinsics.
void vector_add(int *a, int *b, int *c) {
HWY::Simd<int, 8> D;
auto va = HWY::Load(D, a);
auto vb = HWY::Load(D, b);
auto vc = HWY::Add(va, vb);
HWY::Store(D, c);
}
Target Select
(C/C++ Macro)
__riscv_vle32_v_i32m1(ptr, vl)
AVX
NEON
_mm256_load_si256(ptr)
vld1q_s32(ptr); vld1q_s32(ptr+4);
RVV

## Slide 18: Specifications on Member’s Visibility
Specifications of each component in NDP Task by its visibility/scope
 | Member function | Member variable
public | Host-callable APIs | Host-visible data
private protected | device_main(), kernel functions | Device-private data (CXL memory / Scratchpad)

## Slide 19: NDP-Specific Methods
Arachne utilizes Google’s Highway SIMD Library for expressive vector parallelism and extends it to support efficient NDP-specific primitives.
  LoadFromChunk(), StoreToChunk()
    Efficiently load from/store to logically mapped data chunk
  AddOffset()
    Used to compute address of indirectly mapped data
  GlobalUthreadID(), LocalUThreadID()
    Used to identify individual μthreads for advanced algorithms

## Slide 20: Static Instruction Count Reduction
Chart: Static instruction reduction rate
| GEMV | OLAP lt-int64 | OLAP gt-lt-fp32 | OLAP 3-col-and | DLRM | SPMV
 | 0.095238 | 0.14286 | 0.14286 | 0.22222 | 0.075472 | 0
Kernels